## Slide 1: CS4101 嵌入式系統概論 General Purpose IO
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
Materials from MSP430 Microcontroller Basics, John H. Davies, Newnes, 2008

## Slide 2: Recap: MSP430 LaunchPad
Part and Socket
Crystal Pads
Reset Button
P1.3 Button
Chip Pinouts
USB Emulator Connection
LEDs P1.0 & P1.6
Embedded Emulation

## Slide 3: Recap: MSP430 Microcontroller
X
No P3 for 20-pin MCU
P1REN
…
P1IN
P1OUT
MOV.B #0x40,P1OUT
LED
0x21
0x40
0100..0
Notes: Go through all the components once and explain their meanings

## Slide 4: Recap: MSP430 Program for Output
// Blinking both LEDs #include <msp430.h> void main(void) { WDTCTL = WDTPW + WDTHOLD; // Stop watchdog P1DIR ¦= 0x41; // set P1.0 & 6 to outputs for(;;) { volatile unsigned int i; P1OUT ^= 0x41; // Toggle P1.0 & P1.6 i = 50000; // Delay do (i--); while (i != 0); } }

## Slide 5: Outline
MSP430 GPIO
Configuring GPIO
GPIO output
GPIO input
  Problems with input from buttons
Sample code for GPIO input

## Slide 6: MSP430 GPIO
GPIO = General Purpose Input/Output
  Digital I/O
8-bit I/O ports
Each pin is individually controllable
  by memory-mapped registers R1IN, R1OUT, …
 | P1.7 | P1.6 | P1.5 | P1.4 | P1.3 | P1.2 | P1.1 | P1.0
I/O Port 1 | Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0

## Slide 7: Configuring GPIO Ports
Registers (Mem Addr) | Functions | Descriptions
P1IN (0x0020) | Port 1 input | This is a read-only register that reflects the current state of the port's pins.
P1OUT (0x0021) | Port 1 output | The values written to this read/write register are driven out to corresponding pins when they are configured to output.
P1DIR (0x0022) | Port 1 data direction | Bits written as 1 (0) configure the corresponding pins for output (input).
P1SEL (0x0026) | Port 1 function select | Bits written as 1 (0) configure corresponding pins for use by the specialized peripheral (for general-purpose I/O).
P1REN (0x0027) | Port 1 resistor enable | Bits set in this register enable pull-up/down resistors on the corresponding I/O pins.

## Slide 8: PxDIR (Pin Direction): Input or Output
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
P1IN |  |  |  |  |  |  |  | 
P1OUT |  |  |  |  |  |  |  | 
P1DIR | 1 |  |  |  |  |  |  | 
PxDIR.y: 0 = input 1 = output
Register example: P1DIR &= 0x80;
P1IN.7
P1OUT.7
P1DIR.7
“1”

## Slide 9: GPIO Output
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
P1IN | X |  |  |  |  |  |  | 
P1OUT | 1 |  |  |  |  |  |  | 
P1DIR | 1 |  |  |  |  |  |  | 
P1IN.7
P1OUT.7
P1DIR.7
“1”
“1”
“1”
PxOUT.y: 0 = low 1 = high
Register example: P1OUT &= 0x80;

## Slide 10: GPIO Input
Problem occurs if P1.7 is connected to a button!
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
P1IN | 1 |  |  |  |  |  |  | 
P1OUT | X |  |  |  |  |  |  | 
P1DIR | 0 |  |  |  |  |  |  | 
P1IN.7
P1OUT.7
P1DIR.7
“0”
“1”
“1”

## Slide 11: Problem with Input from a Button
When the button is pressed down (closed), MSP430 will detect a 0 from the pin
When the button is up (open), what will MSP430 detect?
Ans.: random value
 Floating

## Slide 12: Typical Way of Connecting a Button
A pull-up resistor Rpull holds input at logic 1 (voltage VCC) while button is up and logic 0 (VSS) when button is down  active low
  But a wasted current through Rpull to ground when button is down  reduced by making Rpull large enough, e.g. 33 k
Also work with pull-down R:
http://www.resistorguide.com/pull-up-resistor_pull-down-resistor/

## Slide 13: Typical Way of Connecting a Button
MSP430 offers internal pull-up/down resistor
PxREN register selects whether this resistor is used (1 to enable, 0 to disable)
  When enabled, the corresponding bit of PxOUT register selects whether the resistor pulls up the input to VCC (1) or down to VSS (0) on button up
Another issue on button: bouncing
  Need to do debouncing

## Slide 14: GPIO Input
Enable resistor
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
P1IN | x |  |  |  |  |  |  | 
P1OUT | 1 |  |  |  |  |  |  | 
P1DIR | 0 |  |  |  |  |  |  | 
P1REN | 1 |  |  |  |  |  |  | 
P1IN.7
P1OUT.7
P1DIR.7
P1REN.7
PxREN enables pull-up/pull-down resistors
PxOUT selects pull-up (1) or -down (0)
Lower cost devices may not provide up/down resistors for all ports
up/down

## Slide 15: Sample Code for Input
#include <msp430.h> #define LED1 BIT0 //P1.0 to red LED #define B1 BIT3 //P1.3 to button void main(void){ WDTCTL = WDTPW + WDTHOLD; //Stop watchdog timer P1DIR = LED1; //Set P1.0 for output P1OUT = LED1; //Turn on red LED P1REN = B1; //Set P1.3 to use internal resistor P1OUT ¦= B1; //Set P1.3 to use pull-up resistor for(;;){ //Loop forever if((P1IN & B1) ==0){ //Is button down? P1OUT &= ~LED1; } // Yes, turn red LED off else{ P1OUT ¦= LED1; } // No, turn red LED on } }
Button is active low: 0down; 1up
Why not
P1OUT = 0;
P1OUT = 1;
Notes: Whenever button is down, turn LED off. Whenever button is up, turn LED on.
P1OUT is not initialized and must be written before configuring the pin for output.
Assume button is active low (0  pressed; 1  depressed)
** Set P1OUT to 0 or 1 will destroy P1.3 setting

## Slide 16: Sample Code for Input
What happen if we add a delay loop inside the for-loop?
What if we want to blink the LEDs at all time instead of just turning them on/off on button up/down?
i = 50000; // Delay do (i--); while (i != 0);

## Slide 17: Summary
GPIO: general purpose input/output
Configuring GPIO
  P1DIR, P1SEL, P1REN
GPIO output
GPIO input
  Problems with input from buttons  pull-down/-up resistor
Sample code for GPIO input
  Continuous looping to check button event  polling